## Slide 1: Lidar in R
Tutorial 1
2024 SciNet Fellows Conference
Kevin Li

## Slide 2: Objectives
Learn about lidar
What is lidar?
Why would you want to use lidar data?
How can I get lidar data?
Learn about processing lidar data
What are common steps in processing lidar data?
Use the lidR package in R to process a lidar dataset

## Slide 3: What is lidar?
Light Detection And Ranging
Active remote sensing
Measure distance of objects from sensor using laser pulses
Distance is measured by time difference
Guo et al. 2021
Notes: - contrasts with passive remote sensing, which uses reflectance of solar energy
- lidar actively emits the energy it measures by sending pulses of laser light and using this to measure the distance of objects from the sensor
- The distance is measure through the time it takes for the emitted pulse to be received back by the sensor
- the distance from objects to the sensor is calculated by knowing the precise location of the sensor and and geometries of the pulse path

## Slide 4: Is it LiDaR or lidar?
Deering, C., & Stoker, J. M. (2014). Let’s agree on the casing of Lidar. LiDAR Magazine, 4(6), 48–51.
“sonar” - 98%
“radar” – 99%
lidar
Notes: - Deering and Stoker looked at this question in 2014 in lidar magazine
- They found some disagreement in the peer reviewed literature but about 2/3 of articles use all lower case lidar
- contrast this with ‘sonar’ – sound navigation and ranging
- and with ‘radar’ – radio detection and ranging

## Slide 5: Why lidar?
https://oceanservice.noaa.gov/facts/lidar.html
Zhou et al. 2022
Notes: Detailed terrain models and bathymetric (underwater terrain) lidar with water-penetrating green light
Vegetation volume and biomass estimation at multiple scales, from global scale (spaceborne lidar); landscape scale to look at forest attributes; local scale to look at vegetation structure
Can be used for agricultural ecosystems, monitoring crop growth, crop phenotyping in a nondestructive way
- recognize individual plant parts using deep learning techniques
Data fusion possibilities – combining lidar data with other remote sensing data to integrate structural info from lidar and spectral info from spaceborne remote sensors
https://oceanservice.noaa.gov/facts/lidar.html
Zhou, L., Li, X., Zhang, B., Xuan, J., Gong, Y., Tan, C., Huang, H., & Du, H. (2022). Estimating 3D Green Volume and Aboveground Biomass of Urban Forest Trees by UAV-Lidar. Remote Sensing, 14(20), 5211. https://doi.org/10.3390/rs14205211

## Slide 6: How can I get lidar data?
Terrestrial lidar
Backpack and mobile lidar
UAV and airborne lidar
Spaceborne lidar
Spatial Extent
Resolution
Low
High
Large
Small
Adapted from Guo et al. 2023
Notes: - lidar data can be collected over multiple scales, different technologies
- this affects the resolution of the data produced and the spatial extent that can be effectively covered
- we will be working with UAV and airborne collected lidar

## Slide 7: National 3D Elevation Program
Nationwide lidar data
Bare earth and 3D point clouds
https://apps.nationalmap.gov/lidar-explorer/#/
https://www.usgs.gov/3d-elevation-program

## Slide 8: Objectives
Learn about lidar
What is lidar?
Why would you want to use lidar data?
How can I get lidar data?
Learn about processing lidar data
What are common steps in processing lidar data?
Use the lidR package in R to process a lidar dataset

## Slide 9
In Rstudio, click terminal tab and type:
mkdir –p /90daydata/shared/$USER/tutorial1_lidr/
  Make your own tutorial1 folder
cd /90daydata/shared/$USER/tutorial1_lidr/
  Go into your new folder
cp -r /project/scinet_workshop2/tutorial1/. .
  Move tutorial data into your folder
ln -s "$(pwd)" ~
  Create a symbolic link to the new folder in your home dir
https://atlas-ood.hpc.msstate.edu/
GitHub Repository:
https://github.com/KevinLi-USDA/lidar_tutorial

## Slide 10: Common steps in processing lidar
Guo et al. 2021
Outlier removal
Ground Point Filtering
Normalization
Individual Plant Segmentation
Vegetation Attribute Extraction

## Slide 11: Progressive morphological filtering
Roussel et al. 2023

## Slide 12: Cloth simulation filter
Roussel et al. 2023

## Slide 13: Visualizing lidR outputs in R
Roussel et al. 2023

## Slide 15: Using parallel processing in lidR

## Slide 16: References
Q. Guo et al., "Lidar Boosts 3D Ecological Observations and Modelings: A Review and Perspective," in IEEE Geoscience and Remote Sensing Magazine, vol. 9, no. 1, pp. 232-257, March 2021, doi: 10.1109/MGRS.2020.3032713.
Roussel, J.-R., Goodbody, T. R. H., & Tompalski, P. (2023). The lidR package. https://r-lidar.github.io/lidRbook/